Solar power for a LoRaWAN gateways

The attempt to develop a low cost solar powered LoRaWAN gateway got off to a rough start. The intent was to provide solar charging to a Raspberry Pi (RPi) Zero gateway with a current load of ~450 mA. The first attempt followed the directions at: https://www.activecountermeasures.com/making-a-solar-powered-raspberry-pi/. This seemed like a reasonable match for our purpose. Unfortunately the Anker PowerCore 26800mAh battery that was recommended did not perform as expected. This battery does not have pass-through charging capabilities so when the battery was charging it was not possible to power the RPi Zero. Next, I looked for a battery with pass-through charging and came across the RAVPower 26800 mAh dual port battery pack. When I tested that battery I was able to run the RPi Zero as the battery was charging but when the battery became full and the charging circuitry stopped charging the battery the power to the RPi Zero was interrupted which resulted in a restart of the RPi Zero. Shortly after a restart the battery would start charging from the solar panel again but would quickly stop charging when the battery was full forcing a restart of the RPi Zero. This was clearly not going to work.

It is quite possible that this problem could be solved by placing a capacitor in the charge circuit so there wouldn’t be an interruption of current flow when the solar charging is turned off but it can be risky tearing apart batteries.

We are now in the process of researching other solar charging configurations and have come to the realization that the lowest cost solution will not work.