Download the SD card image for a Raspberry Pi RAK2245
Click on the appropriate link on this page [https://www.chirpstack.io/gateway-os/install/raspberrypi/] to download the image. I downloaded this file: chirpstack-gateway-os-full-raspberrypi3-20200408112223.rootfs

I used Balena Etcher to burn the Raspberry Pi image to an SD card. Flashing takes a few minutes.

This image has ChirpStack installed so the main steps are to configure your device, set up wireless ssh and configure the ChirpStack Application server using a web-based UI. A good set of instructions can be found here: https://doc.rakwireless.com/rak2245-pi-hat-edition-lorawan-gateway-concentrator-module/connect-the-lora-gateway-with-chirpstack

Accessing the gateways
Once the image is installed you need to access the gateway to set up ssh capabilities. Following the RAK Wireless instructions is one way to do this: https://doc.rakwireless.com/rak2245-pi-hat-edition-lorawan-gateway-concentrator-module/accessing-your-gateway

Before connecting for the first time you need to connect to the RAKWireless access point using the same method you use to connect to a WiFi hotspot. In the terminal use ssh to log into the Raspberry pi: ssh pi@192.168.230.1 the password is raspberry.

Configure the gateway
Type sudo gateway-config
Move the curso to 2 “Setup RAK Gateway concentrator then hit enter. Select “2, Server is ChirpStack” and hit enter. Select “1 ChirpStack Channel-plan configuration” then hit enter. Select “9 US 902-928” and hit enter. Keep the default SERVER IP value of 127.0.0.1 and hit enter. Hit enter again until the main menu appears.

To configure wireless ssh capability move the cursor to “5 Configure WIFI”. Select "2 Enable Client Mode/Disable AP Mode" "4 Add New SSID for Client". Select your country “US United States” then enter SSID () the name of the wireless network) "NETGEAR80" then the passphrase to access that network.

Once you are back in the main configuration menu select “OK” and hit enter.

Restart the Raspberry Pi then log in using ssh. You might need to use a network scanned to get the IP addresss for the Raspberry Pi or if you can a monitor connected to the RPi you can use ifconfig to see the address.

Log into the RPi using ssh
use ssh pi@10.0.0.50 (using your IP address) and the password is raspberry

Access and configure the ChirpStackApplication Server
Once logged in using ssh open a browser on the computer that you ssh-ed from and navigate to: http://10.0.0.50:8080 (this address will need to match your IP address). The username and password are both admin

You can leave most of the settings as is but some must be configured to accommodate the setting used by the terrapin tracker.

Device-profiles
We will add a new profile that uses otaa and Cayenne LPP. Click on “Device-profiles” then click on “+ create” to create a new profile. Enter the following settings. After making the changes click on “CREATE DEVICE PROFILE”.
General
Device-profile name = otaa_cayenne
Network-server = ns
LoRwWAN MAC version = 1.0.2
LoRaWAN Regional Parameters revision = A
Last three fiels are “0”
Join (OTAA/ABP)
Device supports OTAA is checked
CLASS-B
Device support Class-B not checked
CLASS-C
Device support Class-B not checked
CODEC
Payload codec = Cayenne LPP

Applications
We will create a new application and within that we will add a device. Click on “Applications” then “+ CREATE”. Enter the following settings. After making the changes click on “CREATE APPLICATION”.
Application name = neds_gnatApplication
Application description = Application for Gnat testing
Service-profile = service-profile
Payload codec = Cayenne LPP

Integrations
If you want to add an integration such as a server click on the Application you just created then click on “INTEGRATIONS” then “+ CREATE”. Enter the appropriate information. For example:
Kind = HTTP
upllnk data URL = http://64.227.0.108:8300/api/user/
All other field are blank

Devices
To add a device (Gnat) go to “Applications” then click on the name of the application you created in the previous step. Click on “+ CREATE” and enter the following information.
Configuration
Device name = neds_gnat2
Device description = Neds second Gnat
Device EUI = 383434306a379301
Device-profile = otaa_cayenne,
Disable frame-counter validation not checked

After clicking Create Device you need to enter the Application key
Keys (OTAA)
Application key = 9C5E64056A46C2872DED008E20A6F95A
Gen Application key – leave blank
Click on “SET DEVICE-KEYS”

To test if the settings work click on the device link you just created then click on “DEVICE DATA”. Connect a Gnat with a working sketch that will broadcast lora packages and you should see it displayed in the web page.